## Slide 1
OPENCAST MINING EQUIPMENT TECHNOLOGY TRENDS
NOV 12th , 2013 : New Delhi
LARSEN & TOUBRO
REENERGISING INDIAN COAL SECTOR

## Slide 2: Trends
Mining Equipment Size
Equipment Operating Systems
Equipment Tracking Systems
Equipment Management Systems.
Safety Features.

## Slide 3: In Mining, Size matters….

## Slide 4
Loading Tool : Shift
Electric Rope Shovels
Hydrualic Excavator
Electric Rope Shovels deployed by PSU Mining Cos.
Hyd. Backhoes / Shovel (10-34 Cu.M. Class) – Private sector Indian Mining Cos. e.g. Hindustan Zinc, EMTA, Jaypee group, Electro steel, Essel Mining, Mahaan Coal.
PSU Mining Co. (SECL, NCL, SCCL, NMDC) started procuring (10-12 Cu.M.) class HEX.
Tendency to shift to Hyd. Backhoes due to selective mining capability and higher productivity.

## Slide 5
Hauling Equipment – Increasing size
Industry moving to larger payload (up to 240T class) Dump trucks.
Shift took place at PSU mining Cos. like SECL as well as Pvt. Mining Cos (HZL, Reliance, Essar ).
Deployment of large capacity trucks due to significant improvement in Productivity with less manpower.
30 T / 40 T Payload dump trucks
100 T to 240T Payload dump trucks

## Slide 6
Benefits – Large Capacity Equipment
Higher economic life.
Enhanced productivity.
Reduced Manpower.
Reduced Cost per ton.
Reduced in pit Traffic congestion.
Enhanced in pit Safety.
Enhanced Reliability due to proven global technology.

## Slide 7
Equipment Operating Systems

## Slide 8
HYBRID
Intelligent Machine Control.

## Slide 9
Hydraumind : “Hydraulic-Mechanical Intelligent New Design
Integrated Hydraulic & mechanical systems, which supervises the excavators operations.
Not computer dependent & not even essentially electronically controlled.

## Slide 10
Provided optimal solutions benefiting from IT
Reduced environmental impact
Assured safer operating conditions
Supplied powerful, superior-quality equipment
Genuine Answers for Land & Environment Optimization
Notes: Building on the technology and expertise Komatsu has accumulated during more than 85 years of successful business operations: - GALEO presents customers worldwide with a strong, distinctive image of technological innovation and exceptional value. Designed with high productivity, safety and environmental considerations in mind, as it is expressed in "Genuine Answers for Land & Environment Optimization", the machines in this line reflect Komatsu's commitment to contributing to the creation of a better world.
Four elements are contained with the GALEO name, each an essential theme for our business:
  Providing optimal solutions benefiting from information technology;
  Reducing environmental impact;
  Assuring safer operating conditions; and
  Supplying powerful, superior-quality equipment.

## Slide 11
Integrates Electronic , Engine and Hydraulic Technology.
Meets and exceeds latest emission requirements & optimises fuel consumption.
Helps perform heavy duty jobs at all times.

## Slide 12
Hybrid Hydraulic Excavator
Uses electrical components not found in its conventional counterpart : a generator motor, inverter, capacitor and electric swing motor.
Converts large amounts of energy lost in swing motor braking into electric energy & stores it in the capacitor.
Stored energy used to power swing motor or the generator motor.
The generator motor assists the engine in driving the hydraulic pumps.
Saves fuel consumption up to 25%.

## Slide 13
Intelligent Machine Control
Fully Automatic Blade Control For Rough And Fine Dozing
Can perform both rough dozing & finish grading with ease.
Seamless transition from rough dozing to finish grading operation.
Increased efficiency & productivity.

## Slide 14: High Technologies (AHS) –Unmanned Dump Trucks
GLONASS Satellite
GPS Satellite
1) Hauling
- Precise navigation
- High speed and robust control
2) Loading Site
Automatic path generation to loading machine
3) Dumping site
- Paddock dump (Auto path generation)
- Crusher dump (Designated location)
4) Fleet Control
- Flexible and expandable
- Manual vehicle interaction
- Grader interaction
5) Safety
Obstacle detection by millimeter wave radar
6) Operation
- High availability
- Economical
- Reliable
Master LinkTM
Water Truck
Motor Grader
Central Office
How Komatsu’s Autonomous Haulage System Works
Notes: Komatsu promotes the research and development of original leading-edge technologies for commercialization in many areas. One such effort includes the development of an autonomous haulage system (AHS). In this system, unmanned dump trucks equipped with state-of-the-art technologies, such as a high-precision GPS and millimeter wave radar, automatically approach loading equipment and travel along the assigned road to the designated point for dumping. AHS has a high-tech manual interaction function to maintain the safety of vehicles in the AHS area, including other manual vehicles, such as motor graders and water trucks. If a person comes close to the truck, it detects the person with an on-board radar and stops automatically. We believe that this kind of advanced technology will contribute to the improvement of our customer's operations, especially in terms of safety and productivity.
This AHS is just one example of our advanced technologies that we will continue to conduct research and development on into the future.

## Slide 15: Trolley Assist
Power Supply from a Transmission Line rather than a Diesel Engine
Benefits
  Increased Productivity
  Lower Fuel Consumption
  Higher Speed on Grade
Typical Application:
  Uphill Haul Segments
  Established Travel Routes
  Large Diesel Fuel vs. Electric Power Cost Difference
> 100 Operating Trucks Worldwide
Notes: No. of Clicks: 2 - (1) Major Benefits/Increased Productivity (2) Next Slide
Presentation Notes:
- transmission line provides additional power to take advantage of the extra wheelmotor capacity that current diesel engines cannot fulfill.
- maximum 860E wheelmotor capacity ~5200 hp
- Electric wheelmotor design practices address both propel and retarding applications.
* retarding application results in greater power quantities than propel.
* thus extra hp capacity not typically used in propulsion.
#1 – Let’s see how this extra wheelmotor power is used.

## Slide 16: Application Zones
0.05
0.10
0.15
0.20
Power
($/kwh)
0
Diesel
($/liter)
0.20
0.40
0.60
0.80
1.00
1.20
Example 2:
Energy cost $0.10 kwh
Diesel cost: $0.80 / L
Slope Length:
Example 1:
Energy cost $0.15 kwh
Diesel cost: $0.50 / L
Lowest Cost
Option
1000 m
2000 m
Diesel Application
Zone
Trolley Application
Zone
Trolley
Diesel
Lowest Cost
Option
Diesel vs. Trolley
Notes: No. of Clicks: 4 - (1) Diesel App. Zone (2) Example 1 (3) Example 2 (4) Next Slide
Presentation Notes:
#1 - Primary Graph Concept is to define lowest cost/ton option for two key variables:
* Diesel Fuel Cost
* Electric Power Cost
- Trolley Feasibility Readily apparent based on large size of 1000 meter application.
- Trolley Segment Grade = 8% + 1%.
- Diesel Fuel Cons. = 35 lph
- Power Cons. = 3420 kw (1800 v x 1900 amps)
- Trolley System Avail. = 80%

## Slide 17
Equipment Tracking Systems

## Slide 18: KOMTRAX:
Machine Tracking System
This service is not available in certain area.
How KOMTRAX works
Communication Satellite / Mobile Phone
Machine
Data server
Web Application Server
Internet
GPS
User
Distributor / Customer
KOMTRAX Terminal
GPS antenna
Pump controller
KOMTRAX Controller
Engine controller
Communication antenna
Modem
Machine
Notes: KOMTRAX is a machine management system for construction equipment, utilizing web technology.
The main purpose of this system is to reduce customer's operating cost by monitoring service meters, machine positions, working records, warnings, fuel level and others.
The total lifecycle cost of machines consists of machine cost and operating cost. The operating cost includes maintenance, fuel, and the operator's wage. In general, the operating cost is as much as two to three times higher than the machine cost. KOMTRAX aims to lower the operating cost.
The chart at the center of this slide, shows how KOMTRAX works:
Machines are equipped with computers such as a pump controller and an engine controller. Information concerning operating conditions gathered through these controllers is sent to the KOMTRAX terminal. As for machine positioning, KOMTRAX receives the information from GPS satellites.
The collected information is then converted into a data format which our customers can easily see after analyzing the data with web applications. Then the information is transmitted to customers and distributors all over the world.
In 2009, the number of KOMTRAX-equipped machines has topped the 140,000 mark.

## Slide 19
KOMTRAX : Machine Tracking System
Full Machine Monitoring
Complete Machine Status
Total Fleet Management
IMAGINATION
AN
EXPERIENCE
BEYOND
KOMTRAX Reports

## Slide 20
KOMTRAX : Machine Tracking System

## Slide 21: KOMTRAX Plus
Satellite Communication
Gateway Control Center
KOMTRAX Plus data download
KOMTRAX Plus data Wireless download
Machine condition data
Machine operation data
Internet
T/M Severity
Engine Severity
Payload Data
At Distributor
KOMTRAX Plus
Database
KOMTRAX Plus
DATA ANALYSIS
Proactive Support
Prompt communication:
Reduce unscheduled repair.
Accurate forecast:
Extend and optimize major component life.
Reduce cost for repair and maintenance
Keep high machine availability
8
Integrates KOMTRAX & VHMS ( Vehicle Health Monitoring System) for component condition & operation data monitoring on a continuous basis.

## Slide 22
Equipment Management Systems

## Slide 23
GPS Signal
GPS Collection
Survey
Bulldozer Operation System
Digging Operation System
Dump Truck Dispatch System
MINES MANAGEMENT SYSTEM
Modulur Mining
Notes: DISPATCH is the management system for mining operation. DISPATCH is developed by Modular Mining Systems, one of Komatsu group companies. Positioning of machines can be easily identified by GPS-based DISPATCH and enables you to dispatch the right machine to the right place, and optimizes the assignment of the fleet. DISPATCH is used in many mining sites and is the de facto standard on a worldwide basis.

## Slide 24
Mine Management Packages

## Slide 25
Safety Features

## Slide 26
SAFETY FIRST: Features
Rear View Camera and Monitor
Payload Meter
Antilock Brake System (ABS)
Auto Spin Regulator (ASR)
Auto Fire Suppression System (AFSS)
Auto Centralized Lubrication (ACLS)
Vehicle Health Monitoring System (VHMS)

## Slide 27
ARSC
Descending down hill in constant speed without retarding control
Descending speed can be set from 10 km/h to 55km/h
Adjusting pre-set speed ±1 km/h
With Retarder Overheat Caution
Up speed
Down speed
Concentrates on steering control
Improves Efficiency
Reduces operator fatigue
Pre-set vehicle speed
Operation feels like auto-cruise control on automobiles
ARSC (Automatic Retarder Speed Control)
HD785-7

## Slide 28
Operator Cabin With Integrated FOPS
FOPS according to ISO 3449
Falling Objects Protective Structure
protects operator from injury
Test Procedure: 227 kg ( 500 lb )
falling from 5,3 m ( 17‘4“ ) onto
FOPS structure
A mass with the energy of 11600 Joule falling onto the cab roof, should not cause penetration of any part of the FOPS structure
Test result:
positively no penetration

## Slide 29
Continuous display of operating status.
Stored and accessible precise service information for quick trouble shooting, timely service and repairs.
Plain text display for continuous monitoring
Additional acoustic warning with, if necessary, engine shut down
Fault messages stored and can be downloaded
Memory protected with battery back-up
Fault Monitoring and Storage
ETM System
Control Panel :
Security in Operation and Machine Handling
ECS System
VHMS System

## Slide 30
Thank You
30